REQUEST FOR PROPOSAL (RFP)

FOR

INSTALLATION OF A GRINDER PUMP STATION SYSTEM

- INTRODUCTION

The Town of Catskill seeks proposals from construction companies with relevant experience in installation of simplex grinder pump station systems.  Proposals shall be submitted in a sealed envelope, addressed to Supervisor at Catskill Town Hall, 439 Main Street, Catskill NY, 12414 and shall bear on the face thereof the name and address of the respondent and the title “grinder pump station installation”.  Proposals are due no later than 4 pm on November 16, 2020.  Faxed proposals will not be accepted.

The Town of Catskill reserves the right to reject any and all proposals and to select the proposal which, based in its own judgment, will best assure the efficient performance and best quality of work.  Expenses related to the preparation of the proposal shall be borne solely by the contractor submitting the proposal.  Questions related to this RFP should be addressed to Travis Smigel at Delaware Engineering at (518) 452-1290.

- PROJECT DESCRIPTION

As part of the Town of Catskill Sanitary Sewer Collection System Project, the Town of Catskill is requesting lump sum pricing for the installation of a residential grinder pump station system with connection to the newly installed sewer system. The Town will supply the pump station and pump. a diagram of which is attached. Installation of the residential grinder system will include, but are not limited to, the following:

- All excavation and appurtenances for installation of a Town owned grinder pump station and pump.

- Approximately 120’ of 1.25” HDPE DR-11 IPS forcemain piping for connection from grinder system to newly installed forcemain at the roadway.

- Provide check valves at connection point to existing forcemain and at grinder pump station.

- Provide complete connection to electrical panel located at the household.

- Provide 10’ of 4” pvc lateral stub for connection by homeowner. (homeowner may choose to contract with selected contractor for full lateral connection. Any extension of the sewer lateral will be at the sole cost of the property owner.

- Prevailing wage rates are required.

- PROPOSAL SUBMISSION REQUIREMENTS

Interested contractors should provide sufficient information of their qualifications and experience to undertake all tasks associated with the work including but not limited those tasks detailed in the this RFP.  The Town will require the selected contractor to carry out the required tasks in compliance and with qualified understanding of all applicable laws, regulations, and standards, as well as accepted construction standards and practices.